## Slide 1: DIGITAL ELECTRONICS
LOGICAL GATES

## Slide 2
A logic gate is a device that acts as a building block for digital circuits. They perform basic logical functions that are fundamental to digital circuits. Most electronic devices we use today will have some form of logic gates in them. For example, logic gates can be used in technologies such as smart phones, tablets or within memory devices.
WHAT IS LOGICAL GATES

## Slide 3
In a circuit, logic gates will make decisions based on a combination of digital signals coming from its inputs. Most logic gates have two inputs and one output. Logic gates are based on Boolean algebra. At any given moment, every terminal is in one of the two binary conditions, false or true. False represents 0, and true represents 1. Depending on the type of logic gate being used and the combination of inputs, the binary output will differ. A logic gate can be thought of like a light switch, wherein one position the output is off -- 0, and in another, it is on -- 1. Logic gates are commonly used in integrated circuits (IC).

## Slide 4: LOGICAL GATES

## Slide 5
COMPOSITION OF LOGIC GATES
High or low binary conditions are represented by different voltage levels. The logic state of a terminal can, and generally does, often change as the circuit processes data. In most logic gates, the low state is approximately zero volts (0 V), while the high state is approximately five volts positive (+5 V).

## Slide 6
Logic gates can be made of resistors and transistors or diodes. A resistor can commonly be used as a pull-up or pull-down resistor. Pull-up and pull-down resistors are used when there are any unused logic gate inputs to connect to a logic level 1 or 0. This prevents any false switching of the gate. Pull-up resistors are connected to Vcc (+5V), and pull-down resistors are connected to ground (0 V).
Commonly used logic gates are TTL and CMOS. TTL, or Transistor-Transistor Logic, ICs will use NPN and PNP type Bipolar Junction Transistors. CMOS, or Complementary Metal-Oxide-Silicon, ICs are constructed from MOSFET or JFET type Field Effect Transistors. TTL IC's may commonly be labeled as the 7400 series of chips, while CMOS ICs may often be marked as a 4000 series of chips.
Composition

## Slide 7
Basic logic gates
There seven basic logic gates: AND, OR, XOR, NOT, NAND, NOR, and XNOR.
AND | OR | XOR | NOT | NAND | NOR | XNOR