## Slide 1: COMPUTER NETWORKS
TYPES OF NETWORK

## Slide 2: ERROR
An Error is a situation when the message received at the receiver end is not identical to the me
Types Of Errors
Single-Bit Error
Burst Error

## Slide 3: Single-Bit Error
The only one bit of a given data unit is changed from 1 to 0 or from 0 to 1.
Single-Bit Error does not appear more likely in Serial Data Transmission. For example, Sender sends the data at 10 Mbps, this means that the bit lasts only for 1 ?s and for a single-bit error to occurred, a noise must be more than 1 ?s.
Single-Bit Error mainly occurs in Parallel Data Transmission.
For example, if eight wires are used to send the eight bits of a byte, if one of the wire is noisy, then single-bit is corrupted per byte.

## Slide 4: Burst Error
The two or more bits are changed from 0 to 1 or from 1 to 0 is known as Burst Error.
The Burst Error is determined from the first corrupted bit to the last corrupted bit.

## Slide 5: Single Parity Check
Single Parity checking is the simple mechanism and inexpensive to detect the errors.
In this technique, a redundant bit is also known as a parity bit which is appended at the end of the data unit so that the number of 1s becomes even. Therefore, the total number of transmitted bits would be 9 bits.
If the number of 1s bits is odd, then parity bit 1 is appended and if the number of 1s bits is even, then parity bit 0 is appended at the end of the data unit.
At the receiving end, the parity bit is calculated from the received data bits and compared with the received parity bit.
This technique generates the total number of 1s even, so it is known as even-parity checking.

## Slide 6: Drawbacks Of Single Parity Checking
It can only detect single-bit errors which are very rare.
If two bits are interchanged, then it cannot detect the errors.

## Slide 7: Two-Dimensional Parity Check
Performance can be improved by using Two-Dimensional Parity Check which organizes the data in the form of a table.
Parity check bits are computed for each row, which is equivalent to the single-parity check.
In Two-Dimensional Parity check, a block of bits is divided into rows, and the redundant row of bits is added to the whole block.
At the receiving end, the parity bits are compared with the parity bits computed from the received data.