## Slide 1: : 8
Lecture: 18
Complements
(111)2 – (010)2 = (101)2

## Slide 2: Complements
for simplifying the subtraction operation and for logical manipulation.
Two types of complements:
  the r’s complement
  The (r-1)’s complement

## Slide 3: (r-1)’s Complement
Given a number N in base r having n digits, the (r-1)’s complement of N is defined as
(rn - 1) - N

## Slide 4: 9’s complement
the 9’s complement of a decimal number is obtained by subtracting each digit from 9.
The 9’s complement of 546700 is: 453299

## Slide 5: 1’s complement
  the 1’s complement of a binary number is formed by changing 1’s into 0’s and 0’s into 1’s.
e.g. the 1’s complement of 1011001 is 0100110

## Slide 6: r’s Complement
The r’s complement of an n-digit number N in base r is defined as
rn - N for N≠ 0 and 0 for N = 0.
the r’s complement is obtained by adding 1 to the (r-1)’s complement.

## Slide 7: r’s Complement
the 10’s complement of 2389 is 7610 + 1 = 7611  which is adding 1 to the 9’s complement value.
the 2’s complement of binary 101100 is 010011+1 = 010100  i.e. adding 1 to the 1’s complement value.

## Slide 8: 10’s complement can also be obtained by
Leaving all least significant 0’s unchanged
Subtracting the first non-zero least significant digit from 10.
and then subtracting all higher significant digits from 9.

## Slide 9: 2’s complement can also be obtained by:
Leaving all least significant 0’s and the first 1 unchanged.
Then replacing 1’s by 0’s and 0’s by 1’s in all other higher significant bits.

## Slide 10: Subtraction of Unsigned Numbers (M-N)
Add M to the r’s complement of the N.
If M≥N, the sum will produce an end carry which is discarded and what is left is the result M – N.
If M≤N, the sum does not produce an end carry and is equal to r’s complement of (N-M). To obtain the answer in familiar form, take the r’s complement of the sum and place a negative sign in front.