## Slide 1: Non Conventional Solar Pond

## Slide 2: Working Principle
The solar pond works principle that water or air when heated they become lighter and rise upward

## Slide 3: Working
characteristic of solar ponds that allow them to is a salt-concentration gradient of the water. This gradient results in water that is heavily salinated collecting at the bottom of the pond, with concentration decreasing towards the surface resulting in cool, fresh water on top of the pond. This collection of salty water at the bottom of the lake is known as the "storage zone", while the freshwater top layer is known as the "surface zone".
When sunlight is incident on these ponds, most of the incoming sunlight reaches the bottom and thus the "storage zone" heats up. However, this newly heated water cannot rise and thus heat loss upwards is prevented. The salty water cannot rise because it is heavier than the fresh water that is on top of the pond, and thus the upper layer

## Slide 4: Applications
The heat from solar ponds can be used in a variety of different ways. First, since the heat storing abilities of solar ponds are so great they are ideal for use in heating and cooling buildings as they can maintain a fairly stable temperature. These ponds can also be used to generate electricity by driving some organic Rankine engine cycle - simply a turbine powered by evaporating a fluid.
Solar ponds can be used for desalination purposes as the low cost of this thermal energy can be used to remove the salt from water for drinking or irrigation purposes.