## Slide 1: Wave Plates

## Slide 2
Birefringence of crystals can modify the Polarization State of light which is very useful in many applications. This type of optical components are called birefringent wave plates

## Slide 3
The velocities of the extraordinary and ordinary rays through the birefringent materials vary inversely with their refractive indices. The difference in velocities gives rise to a phase difference when the two beams recombine. In the case of an incident linearly polarized beam this is given by
a = 2pt(ne-no)/l
a-phase difference;
t-thickness of wave plate;
ne, no-refractive indices of extraordinary and ordinary rays respectively;
l-wavelength.
At any specific wavelength the phase difference is governed by the thickness of
the wave plate.

## Slide 4: Half Wave Plate
The half wave plate can be used to rotate the polarization state of a plane polarized light.
Suppose a plane-polarized wave is normally incident on a wave plate, and the plane of polarization is at an angle q. with respect to the optic axis. After passing through the plate, the original plane wave has been rotated through an angle 2q.
A half-wave plate is good in rotating the plane of polarization from a polarized laser to any other desired plane . To obtain horizontal polarization, simply place a half-wave plate in the beam with its axis 45° to the vertical.
The l/2 plates can also change left circularly polarized light into right circularly polarized light or vice versa. The thickness of half wave plate is such that the phase difference is l/2 or certain multiple of 1/2-wavelength that is (2n+1)l/2,
        (ne-no) t = l/2

## Slide 5: Quarter Wave Plate
Quarter wave plate are used to turn plane-polarized light into circularly polarized light .. We may do this by orienting an incident plane-polarized wave at 45° to the axis. The thickness of the quarter wave plate is such that the phase difference is l/4 or certain multiple of 1/4-wavelength (2n+1)l/4
(ne-no) t = l/4